## Slide 1: MACOM Diode Products - HMICTM rev 2
Joe Bukowski, Rick Cory
17 March 2017

## Slide 2
Product Families
Diode Products
PIN/NIP Diodes:
Switching
Attenuation
Limiting
Schottky Diodes:
Detection
Frequency Mixing
Attenuators
Varactor Diodes:
Tuning
Phase Shifting
Passive Devices
RF Chokes/Inductors
MNS Capacitors
Resistors
Multiplier Diodes:
Frequency Multiplication
Waveshaping

## Slide 3
Product Configurations
Discrete Device
HMIC Discrete Surmount
(to 26.5GHz)
Beam Lead/ Flip Chip
(to 70+ GHz)
Plastic
(to 6 GHz)
Integrated Solutions

## Slide 4: HMICTM Process
PIN Diode Circuits Schottky Diode Circuits
Passive Networks

## Slide 5: HMICTM = Heterolithic Microwave Integrated Circuit
The HMICTM process comprises pedestals of Si embedded in borosilicate glass
The Si pedestals may form
  PIN diodes
  Schottky diodes
  electrical vias
  thermal vias
The glass features
  low relative dielectric constant (r = 4.1)
  very low loss tangent
  thermal coefficient of expansion well matched to that of Si (TCESi  3.0 ppm/C, TCEglass  3.3 ppm/C
HMIC Surmount Diode

## Slide 6: Simplified HMICTM Process
Start with Si wafer approximately 20 - 25 mils thick
Use photolithography to mask regions of wafer where diodes or vias will be formed
Etch Si in unmasked areas to depth greater than that of final wafer thickness
“Sandwich” glass wafer on top of etched Si wafer and melt glass so it slumps into etched depressions
Cool glass/Si wafer and remove excess glass from top side of wafer to expose tops of Si pedestals
“Wet-Etched” Si Wafer
“Dry-Etched” Si Wafer

## Slide 7: Simplified HMICTM Process (cont’d)
Form diode junctions in tops of Si pedestals
Metalize top surface of glass/Si wafer to
  interconnect diodes
  form passive structures (spiral inductors, capacitors, resistors, transformers, etc.)
Grind back side of wafer to expose underside of glass and Si pedestals
Metalize back side of wafer
Apply benzocyclobutene (BCB) layer to top side for scratch protection
Dice wafer

## Slide 8: HMICTM Cross Section
SPIRAL +
VIA TO GROUND
SERIES PIN
DIODE
SHUNT PIN DIODE
WITH CATHODE BIAS
THERMAL VIA WITH
PASSIVE ELEMENTS
P+ Si
Glass
Si3N4
Metal
N+ Si
I Si
N+ Phos
SiO2
polyimide/ poly-Si
NiCr

## Slide 9: High Frequency Capacitors
Purpose
  Tuning elements
  Block DC voltages
Metal-Nitride-Metal
  Two layers of metal
  Air bridge over dielectric edge
  Q >> 100 @ 2.0 GHz
Interdigitated
  Air dielectric
  Low breakdown voltages
  Small capacitance values
  Single layer of metal
Microstrip Line Stub
  Unterminated (Open)
  <1/4 l at frequency
  Very large at low frequencies
Terminal 2
HMIC Glass
Substrate
Terminal 1
PECVD
Nitride
Dielectric
Terminal 2
Stub
< 1/4 
Microstrip Line
Air
Dielectric
Terminal 1
Air Bridge

## Slide 10: High Frequency Inductors
Metal Lines
  Enhanced mutual inductance between segments
  Parasitic capacitance to ground
Spiral
  Round - higher Q
  Square - max inductance
  Two layer, air bridge metal
  Q » 42 @ 2.0 GHz
Serpentine
  Single level metal
  Low inductive values
  Higher frequency applications
HMIC Glass
Inductor Underpass
Dielectric
Very Low
Parasitic
Capacitance
Backside Ground Plane
Air
Bridge
Mutual
Coupling

## Slide 11: Resistors
Thin film metals
UHVCVD Polysilicon
Typical properties:
HMIC Glass
Deposited Thin Film Metal
Interconnect
Metallization
Metal Ground Plane
Material | Sheet Resistivity | Temperature Coefficient of Resistance
 | (/) | (ppm/C)
NiCr | 5 - 100 | 20
UHVCVD Polysilicon | 10k – 100k | __

## Slide 12: Transmission Lines
Distributed inductors
Provides specific impedance
Microstrip
  Conductor width
  Substrate thickness
  Substrate dielectric constant
Coplanar
  Conductor with adjacent lateral ground planes
  Width & thickness of center conductor
  Spacing to ground planes
  Substrate dielectric Constant
  Area inefficient
HMIC Glass
Metal Conductor
Electric
Field
Lines
Metal Ground Plane
HMIC Glass
Metal Center
Conductor
Electric
Field
Lines
Metal
Ground
Plane
Metal
Ground
Plane

## Slide 13: Typical HMICTM Component Capabilities

## Slide 14: HMICTM PIN Diode Products
Switching

## Slide 15: PIN Diodes
PIN Diodes are current-controlled RF resistors
Primarily used in control circuits
  Switches
  Attenuators
  Limiters
HMICTM PIN diodes are made from Si

## Slide 16: PIN Diode Families
Si Discrete | Si HMIC™ | GaAs | AlGaAs
Wide operating frequency range, to 20 GHz Excellent power handling PIN and NIP diodes available I layer: 2 – 300 µm Available as: Unpackaged chips SMT packages Ceramic Packages Beam leads | Very Wide operating frequency range, to 30 GHz I layer: 8 – 100 µm Available as Single junction devices Multiple junction ICs Wire-bondable or solderable | Wide operating frequency range, to 30 GHz Good power handling Available as: Unpackaged chips SMT packages Ceramic Packages Beam leads | Extremely Wide operating frequency range, to 100 GHz Lower insertion loss than comparable Si or GaAs switches I layer: 3 µm Available as Multiple junction ICs Wire-bondable

## Slide 17: HMICTM Discrete Diode Solution
Part Number | Size (mils) | VB (V) | 1 MHz | 100 MHz |  |  | 1 GHz |  |  |  |  | Lifetime (ns) | Nominal I-region (m)
 |  |  | Cj 40 V (pF) | Rs 10 mA () | Rs 20 mA () | Rs 100 mA () | Cj 40 V (pF) | Rs 10 mA () | Rs 20 mA () | Rs 50 mA () | Rs 70 mA () |  | 
MADP-042305 | 22 X 41 | 80 | 0.13 |  |  |  | 0.14 |  | 1.32 | 1.18 |  | 180 | 7
MADP-042405 | 22 X 41 | 80 | 0.57 |  |  |  | 0.58 |  | 0.62 | 0.58 |  | 255 | 7
MADP-042505 | 22 X 41 | 80 | 0.27 |  |  |  | 0.27 |  | 0.83 | 0.76 |  | 210 | 7
MADP-042905 | 22 X 41 | 80 | 0.06 |  |  |  | 0.06 |  | 3.14 | 2.6 |  | 140 | 7
MA4SPS302 | 23 X 55 | 70 | 0.40 | 1 |  |  | 0.30 | 1.3 |  |  |  | 460 | 10
MA4SPS402 | 20 X 49 | 70 | 0.034 | 4.6 |  |  | 0.04 | 5 |  |  |  | 200 | 10
MADP-017015-1314 | 60 X 30 | 115 | 0.32 |  |  |  | 0.31 | 0.72 |  |  | 0.51 | 1300 | 15
MADP-030015-1314 | 60 X 30 | 115 | 0.79 |  |  |  | 0.78 | 0.49 |  |  | 0.38 | 1600 | 15
MADP-017025-1314 | 60 X 30 | 135 | 0.23 |  |  |  | 0.23 | 1.01 |  |  | 0.64 | 2300 | 25
MADP-030025-1314 | 60 X 30 | 135 | 0.50 |  |  |  | 0.50 | 0.65 |  |  | 0.45 | 2800 | 25
MA4SPS502 | 23 X 57 | 200 | 0.14 |  | 2.4 | 1.4 | 0.09 |  |  |  |  | 2800 | 50
MA4SPS552 | 12 X 22 | 200 | 0.08 |  | 2.4 | 1.7 | 0.06 |  |  |  |  | 2500 | 50
MA4SPS421 | 20 X 41 | 200 | 0.09 |  |  |  | 0.07 | 6.2 |  |  |  | 5000 | 100
MA4SPS422 | 20 X 41 | 200 | 0.18 |  |  |  | 0.13 | 3.1 |  |  |  | 10000 | 100
MADP-042308-1306 | 20 X 41 | 100 | 0.20 |  |  |  | 0.10 |  | 1.38 | 1.18 |  | 280 | 10
MADP-042408-1306 | 20 X 41 | 100 | 0.50 |  |  |  | 0.37 |  | 0.67 | 0.61 |  | 380 | 10
MADP-042508-1306 | 20 X 41 | 100 | 0.30 |  |  |  | 0.18 |  | 0.97 | 0.87 |  | 310 | 10
MADP-042908-1306 | 20 X 41 | 100 | 0.15 |  |  |  | 0.05 |  | 3.63 | 3.02 |  | 230 | 10
Surmount PIN diodes
Available I-region Thickness: 7 to 100 µm

## Slide 18: PIN Switches
Modules Single-Chip

## Slide 19: X-Band Terminated SPDT Switch MASW-011071
Low Insertion Loss: 1 dB
High Isolation: 38 dB
Integrated Bias Network and Termination Circuit
Greater than 20 W CW Power Handling @ 70 °C
Lead (Pb)-Free 7 x 7 mm 44-lead PQFN Package
Missile Defense, Weather Radar Systems

## Slide 20: HMIC Si PIN Switches: 2 W, DC – 26 GHz
Products
  MASW-001100-11900W (SPST)
  MASW002100-11910W (SPDT)
  MASW-003100-19220W (SP3T)
  MASW-004100-11930W (SP4T)
  MASW-005100-11940W (SP5T)
Features
  Operating Frequency
    50 MHz – 30 GHz
  Series-Shunt Configuration
  High Isolation: >35 dB
  Low Loss: <1.0 dB Insertion Loss
  Switching Time: 50 ns
  Max RF Incident Power:
    >6.0 W CW @ 2 GHz
    2.0 W CW @ 22 GHz
  RoHS Compliant
SP5T
SP3T w/ Integrated Bias Network
Notes: 20

## Slide 21: HMICTM Wire-Bondable Switches
Features
SPST through SP6T
Broadband Performance to 26 GHz
Wire /Ribbon Bond Connections
Available With or Without Integrated Bias Networks
SP3T with Bias Network
SP5T without Bias Network

## Slide 22: HMICTM SP2T High Current MASW-011052
Broad Bandwidth: Specified up to 18 GHz, Usable up to 26 GHz
Integrated Bias Network: High Bias Current +/- 60 mA
Low Insertion Loss/High Isolation
Glass Encapsulation Construction
RoHS Compliant and 260 °C Reflow Compatible

## Slide 23: HMICTM SP3T High Current MASW-011053
Broad Bandwidth: Specified up to 18 GHz, Usable up to 26 GHz
Integrated Bias Network: High Bias Current +/- 60 mA
Low Insertion Loss/High Isolation
Glass Encapsulation Construction
RoHS Compliant and 260 °C Reflow Compatible

## Slide 24: HMICTM Package-less Surface Mountable Si PIN Diode Switches
Topology | Frequency | Insertion Loss (dB) | Isolation (dB) | P0.1dB (dBm) | Part Number
SPDT | 6 GHz 13 GHz 20 GHz | 0.6 0.9 1.2 | 45 31 25 | 36 | MASW-002103-1363
SP3T | 6 GHz 13 GHz 20 GHz | 0.65 0.95 1.25 | 37 28 22 | 36 | MASW-003103-1364
SP4T | 6 GHz 13 GHz 20 GHz | 0.7 1.0 1.3 | 35 30 26 | 36 | MASW-004103-1365
Surface mount - No wirebonds
Packageless - Low parasitics
Series/Shunt multi-throw designs
High Power - 6 W incident

## Slide 25: Schottky Diodes
Frequency Mixing Detection

## Slide 26: HMICTM Discrete Schottky Diodes
Features
Surmount Single-Junction Si Schottky diodes
Low, Medium and High Barrier Heights Available
Frequency Range: DC – 30 GHz
Very Low Series Resistance
Very Low Junction Capacitance
Solderable – No Wire Bonds Required
Applications
Mixers and Detectors
Receiver Protector Limiters

## Slide 27: HMICTM Mixer Advantages
Passive, Double Balanced
Silicon Schottky Barrier Diode Ring Quad
Internal Matching at All Ports
Good Port to Port Isolation
Low LO Drive
High IP3 Performance
Small Size
SOT25 Package
NO EXTERNAL COMPONENTS Needed
Monolithically Integrate Low Loss Passives
mmW Frequency Capability
  Smaller
  Lower Cost
  Schottky Diodes NOT Frequency Limited Below 30 GHz

## Slide 28: HMICTM Mixers
Narrowband, Planar, Balun, Low Loss Transformers
Silicon Schottky Barrier Diode Xover Ring Quad
Low, Medium, & High Barrier Height Diodes
Internally Matched
RF
IF
LO
Good port to port Isolation
Passive Double Balanced Mixer
Low LO drive
High IP3 Performance
Small Size
SOT25 Packaging

## Slide 29: Flip Chip Diodes
PIN

## Slide 30: Solderable HMIC Flip Chip PIN Diodes
Parameter | Units | MA4FCP200
Frequency | GHz | Up to 30
Capacitance @ 40 V | pF | 0.020 typical
Series Resistance |  | 2.8 typical
Breakdown Voltage | V | 70 min
Size | µm | 381 X 230
Ultra Low Capacitance
Millimeter Wave Switching & Cutoff Frequency
Silicon Nitride Passivation
Polyimide Scratch Protection
Cu/Ni/Au Solderable Terminals
RoHS Compliant
PIN Diodes - Switching
Parameter | Units | MA4FCP300
Frequency | GHz | Up to 30
Capacitance @ 40 V | pF | 0.080 typical
Series Resistance |  | 2.6 typical
Breakdown Voltage | V | 70 min
Size | µm | 733 X 393
Parameter | Units | MA4FCP300
Frequency | GHz | Up to 30
Capacitance @ 10 V | pF | 0.050 typical
Series Resistance |  | 2.1 typical
Breakdown Voltage | V | 40 min
Size | µm | 733 X 393

## Slide 31: Passive Devices
HMIC™ Bias Networks
Attenuators
MNS Capacitors Spiral Inductors Resistor Networks

## Slide 32: MABT-011000 2-18 GHz HMICTM Surmount Bias Network
HMIC™ Surmount Technology
Broadband Performance 2 – 18 GHz
Parameter | Frequency (GHz) | Target Min | Target Avg | Target Max
Insertion Loss | 2 | - | 0.1 | 0.50
 | 6 |  |  | 
 | 12 |  |  | 
 | 18 |  |  | 
RF – DC Isolation | 2 | 30 | 35 | -
 | 6 |  |  | 
 | 12 |  |  | 
 | 18 |  |  | 
Input Return Loss | 2 | 15 | 17 | -
 | 6 |  |  | 
 | 12 |  |  | 
 | 18 |  |  | 
Output Return Loss | 2 | 15 | 17 | -
 | 6 |  |  | 
 | 12 |  |  | 
 | 18 |  |  | 
High current ±60mA; Voltage ±50V

## Slide 33: Thank You

## Slide 34: Appendix

## Slide 35: Si Mesa Beamlead PIN Diodes
Rugged Silicon-Glass Construction
Silicon Nitride Passivation
Low Parasitic Capacitance and Inductance

## Slide 36: Si Planar Beamlead PIN Diodes
Rugged Silicon-Glass Construction
Silicon Nitride Passivation
Low Parasitic Capacitance and Inductance

## Slide 37: Flip Chip Products
PIN Diodes | Configuration | Max Frequency | Breakdown Voltage Vb | Ct Max | Rs Typical | Material
 |  | (GHz) | (V) | (pf) | () | 
MA4GP907 | Single | 40 | 45 | 0.025 | 4.2 | GaAs
MA4AGP907 | Single | 50 | 50 | 0.020 | 4.2 | AlGaAs
MA4FCP200 | Single | 40 | 50 | 0.015 | 2.8 | HMIC
MA4FCP300 | Single | 30 | 70 | 0.025 | 2.6 | HMIC
MA4FCP305 | Single | 18 | 40 | 0.050 | 2.1 | HMIC
Varactor Diodes | Configuration | Max Frequency | Breakdown Voltage Vb | Ct 4V | Gamma | Material
 |  | (GHz) | (V) | (pf) |  | 
MA46H146 | Single | 60 | 26 | 0.033-0.06 | 1 | GaAs
MA46H120 | Single | 60 | 15 | 0.20-0.40 | 0.5 | GaAs
Low Capacitance Devices

## Slide 38: HMIC and AlGaAs MMIC Performance Comparison
Parameter | HMIC | AlGaAs
Products | Switches, Attenuators, Limiters | Switches
Medium | Silicon and Glass | Semi-Insulating GaAs
Die Thickness (um) | 125 | 100
Intrinsic Length (um) | 8 to 100 | 3
I/O Connections | Wire Bondable and SMT | Wire Bondable Only
Passive R,L,C Integration | Yes | Yes
Breakdown Voltage (V) | 50 to 200 | 70
F (GHz) | 0.050 - 30 | 0.050 - 70
Insertion Loss at 10 GHz (SP4T) | 0.6 | 0.45
Switching Speed (ns) | 100 | 15
IIP3 (dBm) | 45 | 25
CW Power Handling, @ 2 GHz (dBm) | +38 | +28

## Slide 39: HMICTM SP2T 6-14 GHz (Terminated SPDT) MASW-010647
X-Band Terminated SPDT switch
Wire-Bondable Bare Die
Low Insertion Loss/ High Isolation
All Shunt Design; Integrated Bias Network
Glass Encapsulated Construction
Greater than 20 W CW Power Handling @ 85 °C
Silicon Nitride Passivation/Polymer Scratch Protection
RoHS Compliant
Notes: Delete specs table?

## Slide 40: HMIC™ Si PIN SP2T 6-14 GHz MASW-011021
Specified from 8 GHz to 12 GHz ; Usable 6-14 GHz
Low Insertion Loss / High Isolation
All Shunt Design; Integrated Bias Network
Surface Mountable, Fully Monolithic Die
Glass Encapsulated Construction
20 W Pulsed Power Handling
Silicon Nitride Passivation / Polymer Scratch Protection
RoHS Compliant
Notes: Delete Specs Table?