## Slide 1: MACOM Diode Products - Schottky rev 0
Joe Bukowski, Rick Cory
3 March 2017

## Slide 2
PRODUCT FAMILIES
Diode Products
PIN/NIP Diodes:
Switching
Attenuation
Limiting
Schottky Diodes:
Detection
Frequency Mixing
Attenuators
Varactor Diodes:
Tuning
Phase Shifting
Passive Devices
RF Chokes/Inductors
MNS Capacitors
Resistors
Multiplier Diodes:
Frequency Multiplication
Waveshaping

## Slide 3
PRODUCT CONFIGURATIONS
Discrete Device
Bare Die
(to 18 GHz)
HMIC Discrete Surmount
(to 26.5GHz)
Beam Lead/ Flip Chip
(to 70+ GHz)
Hermetic Packaged
(to 12 GHz)
Plastic
(to 6 GHz)
Si HMIC
(to 26+ GHz)

## Slide 4: Schottky Diodes
Schottky diodes are RF/microwave rectifier or switching elements
Schottky diodes are formed by a metal-semiconductor junction
MACOM Schottky diodes are made from Si or GaAs

## Slide 5: Walter Schottky
Swiss/German Physicist, 1886 – 1976
Studied thermionic emission and surface effects in metals and semiconductors
Studied under Max Planck at the University of Humboldt, awarded PhD in physics 1912,
Invented the screen-grid vacuum tube
Taught at the University of Wurzburg and the University of Rostock
Worked at Siemens Research Labs, 1914 – 1919 and 1927 - 1958
Source: https://en.wikipedia.org/wiki/Walter_H._Schottky

## Slide 6: P-N Junction vs. Schottky Junction
Source: Singh, J., Semiconductor Devices: Basic Principles, Chapter 7, Wiley, 2001

## Slide 7: Schottky Diodes
Metal layer has excess electrons
Semiconductor layer
  N type layer is the cathode
  P type (Si only) is anode
junction
n or p semiconductor
metal

## Slide 8: Schottky Diodes
The energy required to move an electron in the semiconductor from the valence band to the conduction band is less than the energy required to move an electron out of the metal
Rectifying junction is formed
eyS
ec
eyM
WV
efB
W0
Electron
Energy
Junction
efSM
metal
semiconductor

## Slide 9: Schottky Diodes
The amount of energy required to cause conduction is determined by the metal-semiconductor combination and is referred to as the barrier height
The forward voltage for a given bias current is proportional to the barrier height

## Slide 10: Metal-Semiconductor Barrier Heights

## Slide 11: Schottky Diode Barrier Heights
Si Schottky Diodes
Four barrier heights available
  High barrier
    Vf at If = 1 mA ~ 0.6 V
    Pt - Si
    n-type substrate
  Medium barrier
    Vf at If = 1 mA ~ 0.33 V
    NiC
    n-type substrate
  Low barrier
    Vf at If = 1 mA ~ 0.25 V
    Ti
    n-type substrate
  Si “Zero Bias Detector”
    Vf at If = 1 mA ~ 0.2 V
    Pd-Si,
    p-type substrate
GaAs Schottky Diodes
Only one barrier height available
  Vf at If = 1 mA ~ 0.7 V, Ti, n

## Slide 12: Schottky Diode I-V Characteristic
For Forward Bias:

## Slide 13: Typical Si Schottky I-V Curves
Typical forward bias curves are shown for
  Si ZBD
  Si low barrier
  Si medium barrier
  Si high barrier

## Slide 14: Schottky Diodes
Schottky diode operation determined by majority carriers (electrons)
No minority carriers are temporarily stored in the depletion region,
  Schottky diodes can switch impedance FAST !!!!!!
Fast switching permits rectification (detectors) and switching (frequency mixers) at RF/microwave frequencies

## Slide 15: Schottky Diode Schematic
Substrate layer typically 100 mm thick
Epi layer typically << 1 mm thick
  Structures are NOT drawn to scale
Multilayer
Metal
Passivation
Depletion
region
Epi Layer
Substrate
Backside
Metal

## Slide 16: Schottky Diode Equivalent Circuit
Backside Metal
Contact
Ohmic Contact
Substrate
Epitaxial
Layer
Thermal Oxide
(SiO2)
Nitride
(Si3N4)
RJ
CJ
RS1
RS2
CO
Top Contact
Metal

## Slide 17: Electrostatic Discharge
Schottky diodes are EXTREMELY sensitive to ESD
  ESD Class 0 (HBM) devices
ESD damage often produces “walking wounded” junction
  Performance deteriorates over time (hours, days or even months)
  Immediate catastrophic failure occasionally occurs

## Slide 18: Schottky Diode Configurations – Singles, Pairs
Single Junction
  single ended mixers
Series Tee
  balanced mixers
Reverse Series Tee
  balanced mixers
Antiparallel Pair
  subharmonic mixers

## Slide 19: Schottky Diode Configurations - Quads
Ring Quad
  Double balanced mixers
Crossover Ring Quad
  Double balanced mixers
  Same circuit as ring quad (above), but easier to build on a single-layer circuit board

## Slide 20: Schottky Diode Configurations – Back-to-Back Crossover Ring Quads
Crossover Ring Quad
  Used for higher-power double balanced mixers
  Two ring quads connected (almost) in parallel

## Slide 21: Schottky Diodes – Specifications of Interest
Capacitance - determined by circuit design
Forward voltage (barrier height) - determined by type of circuit (low power mixer, detector)
Configuration
  single junction, series pair, etc.
Package Style
  plastic, chip-on-board, multi-junction, etc.

## Slide 22: Single-ended Mixer
Lowpass
Filter
LO Input
RF Input
IF Output
RF Choke
Very simple design
  Includes single Schottky diode
Poor inter-port isolation

## Slide 23: Balanced Mixer
RF Choke
Lowpass
Filter
IF Output
RF Choke
RF Input
LO Input
3 dB Hybrid
Includes matched pair of Schottky diodes
Better inter-port isolation

## Slide 24: Subharmonic Mixer
RF Filter
IF Filter
RF Input
IF Output
RF Filter
IF Filter
LO Filter
RF Input
IF Output
LO Input
Actual LO Frequency is Subharmonic of Effective LO Frequency
Schottky diodes multiply input LO frequency AND multiply incoming RF signal by multiples (harmonics) of input LO frequencies
Poor inter-port isolation

## Slide 25: Double Balanced Mixer
IF
Output
RF
Input
LO
Input
Use quad of matched Schottky diodes
  Crossover ring quad saves the customer trouble with circuit board layout
Excellent Inter-port Isolation
Can Function as Phase Detector if LO Frequency  RF Frequency

## Slide 26: Detectors
Detectors produce current waveform whose amplitude is proportional to input signal power
Schottky detectors function as rectifiers
  Half wave uses single Schottky diode
  Full wave uses series tee or reverse series tee
RF in
Detected
Video Out

## Slide 27: Schottky Diode Detector
RF Input Signal is Rectified to Produce Video or DC Output Signal
DC Bias Voltage
RF Signal
Voltage
Detected Current
I
V

## Slide 28: Typical Detector Transfer Function
Square Law
Linear
-60
-40
-20
0
+20
Input Power (dBm)
10 mV
1 mV
10 mV
100 mV
1 V
10 V
Small input signal produces detected output proportional to input signal power (square law detection)
Larger input signal produces detected output proportional to input signal voltage (linear detection)
100 mV
Output Voltage

## Slide 29: Schottky Diode Detector
Low
Pass
Filter
Input
Matching
Network
Video
Amp
L1
C1
DC Bias (optional)
Detector
Diode
RV
RF
Input
Detector
Output
Modulated RF
Input Signal
Detected
Output Signal
Amplitude Detector Using Schottky Diode

## Slide 30: Voltage Doubler Detector
Positive signal alternation charges one capacitor
Negative signal alternation charges other capacitor
Output is taken across both capacitors, effectively doubling detected output voltage
Requires balun structure
RF Input
Video Output
+
-
+
-
+
-

## Slide 31: Temperature Compensated Detector
-
+
R
R
R
R
RF Input
Bias Current
Detected Output
Use two “identical” diodes
One acts as a detector
Other acts as a thermometer
Diodes must be thermally coupled and electrically independent (i.e., an unconnected pair in the same package)
Differential
Amplifier
Detector
Reference circuit

## Slide 32: MACOM Schottky Diode Package Styles
Silicon
Die
  Chip scale
  HMIC
Beam Lead
Surface Mount
  SC-79
  SOD-323
  SOT-23
  SOT-143
  LGA
GaAs
Flip Chip

## Slide 33: Schottky Diodes
Summary
Schottky diodes are metal-semiconductor junction diodes
Used as RF/microwave detectors and mixers
MACOM Schottky diodes are made from Si or GaAs
Barrier height is proportional to forward voltage
  Si: 4 barrier heights available
  GaAs: 1 barrier height available

## Slide 34: Schottky Diodes
Si and GaAs Frequency Mixing Detection

## Slide 35: GaAs Flip Chip Schottky Diodes
Features
Available As:
  Single Junction
  Series Tees
  Reverse Series Tees
  Antiparallel Pairs
  Unconnected Pairs
Low Series Resistance
Low Junction Capacitance
Applications
Mixer and Detector Applications

## Slide 36: GaAs Beamlead Schottky Diodes
Features
Single Barrier Height
Frequency Range: DC – 40 GHz
Available as
  Single Junction
  2-, 4- and 6-Junction Series Tees
  Antiparallel Pairs
  4-, 8- and 12-Junction Ring Quad
Low Series Resistance
Low Junction Capacitance
Applications
Mixer and Detector Applications

## Slide 37: HMICTM Discrete Schottky Diodes
Features
Surmount Single-Junction Si Schottky diodes
Low, Medium and High Barrier Heights Available
Frequency Range: DC – 30 GHz
Very Low Series Resistance
Very Low Junction Capacitance
Solderable – No Wire Bonds Required
Applications
Mixers and Detectors
Receiver Protector Limiters

## Slide 38: Thank You