## Slide 1: MACOM Diode Limiter Products
Rick Cory, Joe Bukowski
3 March 2017

## Slide 2
PRODUCT FAMILIES
Diode Products
PIN/NIP Diodes:
Switching
Attenuation
Limiting
Schottky Diodes:
Detection
Frequency Mixing
Attenuators
Varactor Diodes:
Tuning
Phase Shifting
Passive Devices
RF Chokes/Inductors
MNS Capacitors
Resistors
Multiplier Diodes:
Frequency Multiplication
Waveshaping

## Slide 3
LIMITER PRODUCT CONFIGURATIONS
Discrete Device
Bare Die
(to 18 GHz)
Hermetic Packaged
(to 12 GHz)
Plastic
(to 6 GHz)
Integrated Solutions
Hybrid Solutions
Multichip Modules
(to 8 GHz)

## Slide 4: Transceiver Block Diagram

## Slide 5: Discrete Diodes – Limiters
Limiter diodes can be thought of as RF-voltage-controlled variable attenuators
  When input signal is small,
    limiter diode impedance is high
    RF signal is not attenuated
  When RF signal is large,
    it forces the diode’s impedance to be small
    input signal is reflected back to its source

## Slide 6: Discrete Diodes – Limiters (cont’d)
No external control signal is required for the limiter to operate
DC current return path (e.g., RF choke) is required
Diode I layer thickness determines input power level at which the limiter “turns on”
  Threshold level = input 1 dB compression point

## Slide 7: PIN Diode Parameters for Limiters
Shunt
Diode
Capacitance determines insertion loss
I layer thickness determines
  Threshold level (input 1 dB compression point)
  Spike leakage
  Recovery time
Resistance determines flat leakage
TAKEAWAY: Limiter design is not done with simulators —experience is required!

## Slide 8: Limiter Performance vs. Time
A limiter diode cannot go into conduction instantaneously
  Leading edge of large RF signal is initially unattenuated resulting in spike leakage
As charge carriers accumulate in limiter I layer
  Series resistance decreases
  Attenuation increases due to mismatch loss
When the diode’s resistance reaches equilibrium,
  some power is passed by the limiter
  a small portion of the incident power is dissipated by the diode
  the remainder is reflected to its source

## Slide 9: Junction Heating – the Enemy of All Semiconductors
When the limiter diode is conducting, Joule heating (IRF2RS) causes the junction temperature to rise
The diode acts as a network containing thermal resistance (JC) and thermal capacitance (Cthermal)
Junction temperature rises according to the thermal time constant of the diode
The maximum rated junction temperature for a Si PIN diode is 175 C

## Slide 10: Junction Heating – the Enemy of All Semiconductors (cont’d)
The relation of pulse width of the input signal to th is critical
If pulse width is approximately 3 x or more, heating is roughly equivalent to that caused by a CW signal
Chart: Junction Temperature Rise

## Slide 11: Junction Heating – the Enemy of All Semiconductors (cont’d)
The relation of duty cycle to th is critical
  If duty cycle is too large, due to insufficient cooling times successive pulses cause peak junction temperature to sequentially increase
Low Duty Cycle
High Duty Cycle

## Slide 12: Discrete Diodes – Limiters
Limiter diodes available
  Die Versions (to 20 GHz)
  In Ceramic & Plastic Packages (up to 12 GHz)
  Low Capacitance
  I layers from 2 µm to 40 µm
  Cascadable for Increased Power Handling and Limiting
    Thinnest diode placed at output stage
      Determines threshold level, spike leakage
    Thickest diode placed at input stage
      Determines power handling, recovery time
/4
I standing wave
V standing wave
Thin “clean-up” limiter
Thick “coarse” limiter

## Slide 13: Limiter Products

## Slide 14: Receiver Protector Limiter
Limiter Modules
  Frequency 500 MHz – 8 GHz in octave bands
  Power handling up to 200 W CW, 2 kW peak
  Threshold level as low as 7 dBm
  Non-hermetic:
    5 x 8 mm SMT ceramic package
  Hermetic
    6 x 10 mm SMT ceramic package
Modules and Discrete Limiter Diodes
Limiter Diodes
  Frequency: 50 MHz – 18+ GHz
  I layers from 1.5 to 40 µm
  Power handling: up to 200 W CW, 2 kW peak
  Available in many package styles:
    Chip
    Ceramic package
    Plastic SMT

## Slide 15: Limiter Diodes

## Slide 16
Discrete Limiter Products
Schottky-Limiter-PIN Shunt Antiparallel Pair
Shunt Limiter PIN
Limiter PIN
Broadband Performance to 12 GHz and Higher
Several Packages Available Including
  Low Inductance Shunt Configuration Plastic 1.5 X 1.2 mm DFN
  Ceramic
  Chips
Cascadable

## Slide 17: Discrete Diodes – Limiters
Die Versions (operate to 20+ GHz)
  Available in Ceramic & Plastic Packages (operate to 12+ GHz)
  Low Capacitance
  Cascadable for Increased Power Handling and Limiting
  Au-doped and non-Au-doped diodes available to optimize recovery time and flat leakage power
Part Number | Min VB | Max VB | Min Cj @ 0 V | Max Cj @ 0 V | Max Rs @ 10 mA | Nominal Characteristics |  |  | 
 |  |  |  |  |  | Carrier Lifetime | Intrinsic Region Thickness | Contact Diameter | Thermal Resistance
 | V | V | pF | pF |  | ns | m | mils | ºC/W
MA4L011-134 | 15 | 35 | 0.08 | 0.18 | 2.10 | 10 | 2 | 1.2 | 175
MA4L021-134 | 20 | 35 | 0.10 | 0.20 | 2.10 | 10 | 2 | 1.2 | 175
MA4L022-134 | 20 | 35 | 0.09 | 0.19 | 2.00 | 10 | 2 | 1.2 | 175
MADL-011009-0134 | 20 | 35 | 0.16 | 0.23 | 1.50 | 10 | 2 | 3.0 | 175
MA4L031-134 | 30 | 50 | 0.14 | 0.21 | 2.00 | 20 | 3 | 1.4 | 150
MA4L032-134 | 30 | 50 | 0.13 | 0.20 | 2.50 | 15 | 3 | 1.5 | 150
MADL-011010-0134 | 30 | 50 | 0.17 | 0.24 | 1.50 | 15 | 3 | 3.0 | 150
MA4L062-134 | 60 | 75 | 0.07 | 0.15 | 2.50 | 10 | 4 | 1.5 | 150
MADL-011011-0134 | 60 | 75 | 0.05 | 0.17 | 2.30 | 10 | 4 | 3.0 | 150
MA4L101-134 | 100 |  |  | 0.15 | 2.00 | 90 | 13 | 3.5 | 30
MADL-000301-0134 | 200 |  |  | 0.20 | 1.50 | 200 | 20 | 3.0 | 30
MA4L401-134 | 250 |  |  | 0.30 | 1.20 | 800 | 25 | 4.5 | 25

## Slide 18: Discrete Diodes – Limiters (cont’d)
Die Versions (operate to 20+ GHz)
  Available in Ceramic & Plastic Packages (operate to 12+ GHz)
  Low Capacitance
  Cascadable for Increased Power Handling and Limiting
Part Number | Min VB | Max VB | Typ Cj @ 0 V | Max Cj @ 6 V | Typ Rs @ 10 mA | Nominal Characteristics |  |  | 
 |  |  |  |  |  | Carrier Lifetime | Intrinsic Region Thickness | Contact Diameter | Thermal Resistance
 | V | V | pF | pF |  | ns | m | mils | ºC/W
MLP7100 | 20 | 45 | 0.2 | 0.15 | 1.5 | 5 |  |  | 100
MLP7101 | 20 | 45 | 0.5 | 0.3 | 1.2 | 10 |  |  | 80
MLP7102 | 20 | 45 | 0.7 | 0.5 | 1.0 | 10 |  |  | 55
MLP7110 | 45 | 75 | 0.2 | 0.15 | 1.5 | 10 |  |  | 80
MLP7111 | 45 | 75 | 0.5 | 0.3 | 1.2 | 15 |  |  | 60
MLP7112 | 45 | 75 | 0.7 | 0.5 | 1.0 | 20 |  |  | 40
MLP7120 | 120 | 180 | 0.2 | 0.15 | 1.5 | 50 |  |  | 40
MLP7121 | 120 | 180 | 0.6 | 0.3 | 1.2 | 50 |  |  | 20
MLP7122 | 120 | 180 | 0.8 | 0.5 | 0.5 | 100 |  |  | 15
MLP7130 | 15 | 30 | 0.12 | 0.10 | 2.0 | 5 |  |  | 120
MLP7131 | 15 | 30 | 0.2 | 0.15 | 1.5 | 5 |  |  | 80
MLP7140 | 30 | 60 | 0.12 | 0.10 | 2.0 | 7 |  |  | 100
MLP7141 | 30 | 60 | 0.2 | 0.15 | 1.5 | 7 |  |  | 70

## Slide 19: Limiter Modules

## Slide 20: High Power Limiter Modules
Industry-leading input power handling as high as
  250 W CW
  1 kW peak
No external control signal or external bias required
Available as
  Single stage
  Dual stage
  Detector/limiter
Available in VHF, UHF, L, S and C bands
Packaged in low-thermal-resistance surface-mount hermetic or nonhermetic module packages
Custom designs are possible

## Slide 21: Limiter Modules Maximum CW Power vs. Frequency
Chart: Frequency (GHz)
| 0.01 | 6
MADL-011021 | 34 | 34
LM202602 | 36 | 36
LM501102 | 37 | 37
LM200802 | 44 | 44
LM202802 | 45 | 45
LM401102 | 50 | 50
LM102202 | 50 | 50
LM202402 | 50 | 50
MADL-011014 | 53 | 53
MADL-011012 | 54 | 54

## Slide 22: What’s Inside a Limiter Module? MADL-011014

## Slide 23: What’s Inside a Limiter Module? LM202402-Q-B-301

## Slide 24: Electrical Overstress: A Very Bad Idea…

## Slide 25: Coarse Limiter Stage Damage Due to Electrical/Thermal Overstress

## Slide 26: Summary
A (receiver protector) limiter is a passive device whose insertion loss is controlled by the magnitude of the input signal
  Small signal produces low insertion loss (< 1 dB)
  Large signal produces large isolation (> 30 dB)
  No external control signal is required
MACOM offers limiters comprising our limiter PIN diodes and other components
In order to select a limiter module or diode, we must know:
  Frequency range of operation
  Peak input power
  Pulse width
  Duty cycle
  Acceptable insertion loss, spike and flat leakage levels

## Slide 27: Thank You