## Slide 1: MACOM Diode Products – NLTL Comb Generators rev 0
Joe Bukowski, Rick Cory
11 April 2017

## Slide 2
Product Families
Diode Products
PIN/NIP Diodes:
Switching
Attenuation
Limiting
Schottky Diodes:
Detection
Frequency Mixing
Attenuators
Varactor Diodes:
Tuning
Phase Shifting
Passive Devices
RF Chokes/Inductors
MNS Capacitors
Resistors
Multiplier Diodes:
Frequency Multiplication
Waveshaping

## Slide 3
Product Configurations
Packaged Solutions

## Slide 4: Comb Generators
SRD
NLTL

## Slide 5: Comb Generation
A comb generator produces even- and odd-order harmonics of an input signal
Comb generation requires a nonlinear impedance (NLZ) device to distort the input sinusoidal signal
Step recovery diodes (SRDs) have been used as NLZ devices
Varactor diodes are NLZ devices

## Slide 6: Step Recovery Diode Comb Generators

## Slide 7: SRD Structure and Operation
An SRD is a 3-layer device, similar to PIN diode
  Middle layer of SRD has higher n-type dopant concentration than I layer of PIN diode
Under forward bias, center layer stores charge
As input signal reverses polarity
  Initially, charge is conducted from diode and its impedance remains low
  When large majority of charge is removed, hole-electron recombination becomes dominant and diode “snaps off” (impedance transitions from very low to very high)
SRD parameters
  Carrier Lifetime (TL or )
  Transition time (TT)
    AKA snap time (TS)
  Junction capacitance (CJ)
  Reverse breakdown voltage (VB)
Howell, C.M., Selection of Multiplier Diodes, AN3023

## Slide 8: SRD Frequency Multiplier
SRD frequency multiplier
  Input Z match, LPF structure
  SRD impulse generator
  Output Z match, filter structure
SRD performance is highly wafer-lot-dependent
  Performance is not amenable to simulation
SRD parameter selection
  Carrier Lifetime (TL or )
      10 x Tfundamental
  Transition time (TT)
    TT << Tharmonic
  Junction capacitance (CJ)
    XCJ  50  @ Tharmonic
  Reverse breakdown voltage (VB)
    VB > Vpk @ fundamental frequency
Howell, C.M., Selection of Multiplier Diodes, AN3023

## Slide 9: SRD Frequency Multiplier - Operation
Low frequency input signal drives SRD into conduction during its positive alternation
Charge stored in the diode
While negative alternation conducts charge from diode its impedance remains low
When recombination dominates, the diode’s impedance rapidly goes from low to very high
This change causes the current through the inductor to (almost) instantaneously go to 0 A
Abrupt change in current through the inductor produces a (non-ideal), harmonic-rich voltage impulse
Howell, C.M., Selection of Multiplier Diodes, AN3023

## Slide 10: SRD Multiplier Performance
Difficult to design Z match circuit
  In conduction, SRD impedance is approximately 5 to 10 
  After snap occurs, SRD impedance is very large and capacitive
Performance is highly dependent on input power
  17 dBm ≤ PIN ≤ 33 dBm
Output spectrum has sinx/x envelope
Output power  fundamental input power/harmonic order
Recombination is inherently stochastic
  Produces jitter in time domain  phase noise in frequency domain
Output Spectrum of SRD Comb Generator
A Simple Low Cost Comb Generator Frequency Calibrator, Martin, L, Ham Radio, July 1988

## Slide 11: Nonlinear Transmission Line Comb Generators

## Slide 12: MACOM Low Phase Noise Comb Generators
Low phase noise comb generator product line is based on Non-Linear-Transmission-Line (NLTL) technology.
Review: a single-impedance transmission line comprises a uniform value of inductance and capacitance per unit length
In a practical nonlinear transmission line, the fixed capacitance per unit length is replaced with a nonlinear capacitance

## Slide 13: NLTL Comb Generator Composition
The MACOM family of NLTL comb generators utilize GaAs Schottky varactors diodes (STVARs)
Required doping profile of STVARs for NLTL comb generators is difficult to produce and must precisely meet requirements
Schottky diodes are utilized because they are majority carrier devices – no minority charge carrier storage can occur
  The capacitance of the STVAR can change extremely rapidly (single picoseconds order of magnitude)
  No shot noise is generated
  Much less phase noise is produced

## Slide 14: NLTL Operation
The velocity of propagation along the NLTL is a function of signal voltage due to the presence of the STVARs
  Large signal voltage  small STVAR capacitance  fast velocity of propagation
  Small signal voltage  large STVAR capacitance  slow velocity of propagation
Low voltage portion of incident pulse is increasingly delayed with respect to high voltage portion as the wave front propagates through the NLTL
Fourier analysis of resulting waveform shows spectrum rich in harmonics
Nonlinear Transmission Lines for Picosecond Pulse, Impulse and Millimeter-Wave Harmonic Generation, Case, M. G., PhD Thesis, UCSB, July 2, 1993

## Slide 15: NLTL vs. SRD Comb Generator Output Spectrum
SRD Comb Generator
NLTL Comb Generator
Output Spectrum of SRD Comb Generator
A Simple Low Cost Comb Generator Frequency Calibrator, Martin, L, Ham Radio, July 1988
Output Spectrum of NLTL Comb Generator

## Slide 16: NLTL vs. SRD Comb Generator Phase Noise
Phase noise of NLTL comb generator as much as 15 dB lower than that of SRD comb generator

## Slide 17: Cross-Correlated Interferometer Test System
Cross-correlation capable of removing uncorrelated noise due to mixers and post amplifiers
Uncorrelated noise reduced by 5Log(N) where N is the number of samples. 1000 samples lowers noise floor -15 dB.

## Slide 18: Cross-Correlation Phase Noise Test System

## Slide 19: Non-Linear Transmission Line Comb Generators
NLTL Comb Generators offer key advantages relative to “typical SRD” products:
  Lower phase noise – improved phase noise performance of multiplied source
  Lower input power – reduced PA requirements and power consumption
  Range of input frequency – enables use of single part in several designs or use with a tunable source (up to 3x instead of a few %)
  Higher harmonic power at higher frequencies – SRD-based comb generators output power rapidly rolls off above 20 GHz
  Reliable construction – based on monolithic circuits

## Slide 20: Package Outline Drawings

## Slide 21: Thank You